PROM Installation Guide

Lynx Console Control Unit

TIMELINE VISTA, INC.

1755 LA COSTA MEADOWS DRIVE, SUITE B

SAN MARCOS, CA  92069

TEL. 760-761-4440

(FAX 760-761-4449)

SUPPORT@DIGAUDIO.COM

DATE:	7/13/92

MODEL:	Lynx Console Control Unit (CCU)

REVISION:	All

SERIAL NO:	All

SOFTWARE:	CCU PROM	U3

REQUIRED TOOLS:

Static safe workstation	IC Extractor/Insertor or 
	Grounding wrist strap	small slotted screwdriver
	Phillips screwdriver

REQUIRED PARTS:

Replacement PROM from TimeLine

PROCEDURE:

1.	Turn off the power to the Console Control Unit. Disconnect all cables.

2.	Remove the CCU from the console and place on a static safe workstation. Ground yourself and the workstation 
anti-static mat.

3.	Locate U3, remove and replace the PROM. Be careful to correctly align 
pin one and properly seat the PROM.

4.	Check that jumper JP4 is in the 512K position.

5.	Reinstall the CCU into the console.

6.	Reconnect the cables and turn on the power.  The CCU will automatically detect the new software version. To verify that the upgrade is operating, the new software version number 
will be displayed after turning the power on.

Figure 1.  Location of Jumper and PROM