# Key Cap Installation Guide

## Keyboard Control Unit

TIMELINE VISTA, INC.

1755 LA COSTA MEADOWS DRIVE, SUITE B

SAN MARCOS, CA  92069

TEL. 760-761-4440

(FAX 760-761-4449)

SUPPORT@DIGAUDIO.COM

### DATE:	8/3/92

### MODEL:	Keyboard Control Unit (KCU)

### REVISION:	All

### SERIAL NO:	All

### SOFTWARE:	K600, KCU080-20 and higher

### REQUIRED TOOLS:

Small slotted screwdriver

### REQUIRED PARTS:

SOLO Key Cap - Part No. 50G065

### DESCRIPTION:

The function of the STAT key has been changed to SOLO in K600 Varispeed Software and KCU080-20 and higher software.

### Procedure:

1.	Using a small slotted screwdriver, gently lift the front of the green key cap, as indicated in Figure 1, and remove.

KCU006A

Figure 1.  Key Placement

2.	Position the new key cap on the switch and press down until it clicks into place.