# PROM Installation Guide

Lynx Time Code Module

TimeLine Vista, Inc.

1755 LA COSTA MEADOWS DRIVE, SUITE B

SAN MARCOS, CA  92069

TEL. 760-761-4440

(FAX 760-761-4449)

SUPPORT@DIGAUDIO.COM

### DATE:	9/15/92

### MODEL:	Lynx Gearbox Processor

### REVISION:	All

### SERIAL NO:	All

### SOFTWARE:	V600 & VT600 Series

### REQUIRED TOOLS:

Static safe workstation	IC Extractor/Insertor or
Grounding wrist strap	small slotted screwdriver
Phillips screwdriver

### REQUIRED PARTS:

Software Upgrade Kit

### PROCEDURE:

1.	Turn off the power to the Lynx Time Code Module.  Disconnect all cables.

2.	Place the Lynx on a static safe workstation.  Ground yourself and the workstation anti-static mat.

3.	Remove the six phillips screws holding the top cover to the chassis and remove.  (See Figure 1)

Figure 1.  Remove the Top Cover

4.	Locate and remove the gearbox processor PROMs U7 and U6, if supplied.  
(See Figure 2)

Warning

Use an IC inserter to remove U7 and U6, if supplied.  If one is not available, use a small slotted screwdriver.  Insert the screwdriver under the IC's, twist slightly and gently lift up.  Inserting the screwdriver incorrectly could damage surrounding components.

### PROCEDURE continued:

Figure 2.  Component Location

5	Install the new PROM into U7 and if necessary, U6.  Be careful to correctly align Pin 1 and properly seat the PROM.

6.	Check all connections and replace the cover on the Lynx Time Code Module.  Insert and tighten the six phillips screws.  Reconnect the cables and turn on the power.  The Lynx module will automatically detect the new software.  To verify that the upgrade is operating, the new software version numbers will be displayed first after turning the power on.