Service Bulletin No. 95-003

Optional	TIMELINE VISTA, INC.

1755 LA COSTA MEADOWS DRIVE, SUITE B

Recommended - Not for general distribution	SAN MARCOS, CA   92069

Tel. 760-761-4440

Mandatory	(FAX 760-761-4449)

SUPPORT@DIGAUDIO.COM

## System Supervisor Main PCB Modification

### DATE:	04/05/95

### MODEL:	System Supervisor Unit (SSU)

### REVISION:	All

### SERIAL NO:	All Units prior to Serial Number 243

### SOFTWARE:	All

### REQUIRED TOOLS:

Static safe workstation	Phillips screwdriver
Grounding wrist strap

### DESCRIPTION:

Recently some SSU’s were found to be experiencing problems locking with Lynx-2 modules.  This is due to the SSU not sending out the correct 30Hz Bipolar Output.

### PROCEDURE:

1.	Turn off the SSU and disconnect all cables from the rear panel.  Place the SSU on a static safe workstation.  Ground yourself and the workstation anti-static mat.

2.	Remove the eight phillips screws securing  the top cover of the SSU.  Remove the top cover.

3.	On the Main PCB, locate U26 and U63.  If these IC’s are SGS Thompson HCF 4520 parts, contact TimeLine for an RMA Number, they must be replaced.

4.	Replace the top cover on the SSU.  Insert and tighten the screws.